## Slide 1: Co-Optimization of Fuels & Engines
FOR TOMORROW’S ENERGY-EFFICIENT VEHICLES
Co-optimizer development plan and strategy

## Slide 2: Overview and design goals
Evaluate the merit of an arbitrary combination of biofuel pure components and traditional refinery blendstocks
Import constituent property values from the fuel properties database
Import integer (bin) metrics from market transformation and ASSERT analysis
Identify the composition of constituents that maximizes merit for a specified cost constraint
Be extensible to highly non-linear blending models as well as accounting for uncertainty in blending or merit function

## Slide 3: Overview and design goals
Evaluate the merit of an arbitrary combination of biofuel pure components and traditional refinery blendstocks
Import constituent property values from the fuel properties database
Import integer (bin) metrics from market transformation and ASSERT analysis
Identify the composition of constituents that maximizes merit for a specified cost constraint
Be extensible to highly non-linear blending models as well as accounting for uncertainty in blending or merit function

## Slide 4
Task G.3: Co-Optimizer ($350K $175)
Objectives: Optimize property combinations for cost function with user-defined weights for performance and cost metrics (e.g., MMF value, cost of production, infrastructure compatibility) Integrate data from experiments, simulation, techno-economic and MT factors in decision support tool Scenario analysis for Thrust 1 fuels Approach: Formulate optimization tool Use current available data and propagate available sensitivities to identify optimal fuel property combinations and sensitivities (Thrust 1 engines) Expand on blending studies in G.1 to demonstrate feasible blending strategies for Co-Optima identified properties
Team: Simulation Toolkit Development Task Summary New Continuing from FY16 Proposed FY17 Funding: BETO _____ VTO_____ Lead PI (lab): Grout (NREL; 150K 100K) Participating Labs: ANL(100K 50K), LBNL(50K 25K), LLNL(50K) Thrust I Thrust II Relevant to Both Priority : Base Margin Over Target
Milestones and Outcomes: FY17/Q1 – Initial internal release Outcomes at Base Funding: Identify fuel blend that maximize Miles Merit Function using linear blending rules for an example scenario (NLP problem, linear constraints) Include ASSERT and MT metrics in example scenario as constraints (MINLP problem) Margin Funding Consider uncertainty in merit function (stochastic optimization); determine if multiple indistinguishable optima exist. Convert cost constraint into secondary objective and find Pareto front
Budget:
Project | FY16 | FY17 | FY18 | FY19
VTO | - | B: $225K M: $400K | TBD | TBD
Project Type | Directed |  | Project Status | Continuing
Key link to FY17 Research Thrusts This task is central to key research thrust #3 Key links to other teams Through G.4, ingest data from experimental and simulation data, database from FP and LGGF teams and MT/ASSERT metrics. Provide scenario analysis to CoOLT.
Notes: Without G.4, the “merit function” for engine performance is basically the miles merit function postulated, possibly with coefficients adjusted to better match available data. G.4, on the next page, is the part that rigorously ingests the engine and simulation datasets and puts error bounds on the resulting merit function evaluation for an arbitrary property combination necessary as an input to make this optimizer valuable – especially for choosing new test points that focus research where it most effectively builds confidence in the estimate to distinguish between the multiple possible optima.
Base breakdown: NREL $100k; LLNL $25k; LBNL $50K; ANL $50K
Margin increments: NREL $50k; LLNL $25k; ANL $50K

## Slide 5
Co-Optima Problem
Maximize engine merit function
Constrain integer functions
Subject to:
Cost < cost*
Number of components < n*
With large number of potential constituents to draw from
Notional Refinery problem
Minimize cost
Subject to
RON > 91
RVP < 4
MON > 92
Production > xx gal/day
With relatively few (~6) constituents

## Slide 6
Co-Optima Problem
Multi-objective
Objective function non-linear function of composition or integer valued
Single point (no resource scheduling)
MINLP
Uncertainty in objective function
Uncertainty in contributions to objective function
Notional Refinery problem
Single objective
Goodness function linear
Integral objective (over time for scheduling)
Constraints may be non-linear
Production target externally constrained
LP+bias or NLP
Deterministic (uncertainty ignored in scheduling, handled by on-line controller)

## Slide 7
Unbounded
Maximize by inspection with
High RON
High SL
Low LFV150
Low PMI
S, HOV, ON… it depends
Properties may be correlated
Non linear in function and in properties
To first order, sorting fuels by merit/$ would give us a shortlist
Something interesting to do if fuels with high RON/$ are different from fuels with high SL/$ and LFV150/$

## Slide 8: Fuel property blending
RON / MON / ON
Linear blending models
Blending octane numbers (Ref: Gary & Handwerk ‘94)
Transformation method (Rusin et al. ‘81)
Linear by mole (Knopp et al., ‘14)
Regression based (empirical fit; e.g., Oduola and Iyaomolere ’15)
Non-linear blending models
Olefin content method (Stewart, ‘59)
Ethyl RT-70 (Healy et al., ‘59)
Excess method (Muller, ‘92)
Interaction method (William, ‘75)
Artificial neural networks (NL empirical, e.g., Pasadakis et al. ‘06)
  Many samples: e.g.: Pasadakis used 173 samples for a 7 component blend, RON 93.5-99.0

## Slide 9
Flame speed
Linear by energy fraction
PMI
Definition applies to blends
Ongoing work (elsewhere) to refine definition
HoV
Linear
Vapor pressure
Significant (and ongoing) study
Cost
Linear by traditional definition
L. Sileghem, V. Alekseev, J. Vancoillie, E. Nilsson, S. Verhelst, and A. Konnov. Laminar burning velocities of primary reference fuels and simple alcohols. Fuel, 115:32 – 40, 2014.

## Slide 10: Optimizing engine efficiency merit function
Initial proof of concept + what type of information can we get?
Could run a multi-objective analysis and extract cost vs merit Pareto front
  Or, since there are only two here… re-run analysis for range of c*
Setting this up in Python + pyomo
  Python: evaluate blend properties, mmf, read in properties from list of 20 (or properties database), assert and MT metrics, evaluate constraints
  pyomo: model formulation and assembly
Open source solvers (IPOPT, GLPK...).
  Easy to swap for commercial solvers (CONOPT, CPLEX) using same pyomo formulation
Set this up and testing with “synthetic” properties
  First cut: non-linear objective, linear blending

## Slide 11: List of artificial 20
This is fiction: the ONLY purposes are to have some way to test the optimizer and
to see what type of data we could get out of it once the properties are available
CAS | NAME | FORMULA | MOLWT | BP | LHV | RON | S | HoV | SL | LFV150 | PMI | ON | COST
67-56-1 | Methanol | CH4O | 32040 | 6 | 25 | 109 | 20 | 1173.533084 | 35 | 0 | 1.2 | 89 | 13
71-36-3 | 1-Butanol | C4H10O | 74120 | 117.7 | 33 | 98 | 13 | 708.3108473 | 32 | 0 | 2.8 | 85 | 1.3
k | 2-methyl-butanol | C5H12O | 88150 | 128 | 40 | 101 | 0 | 613.7266024 | 34 | 0 | 1.9 | 101 | 2.9
78-92-2 | 2-butanol | C4H10O | 74120 | 99.5 | 18 | 107 | 14 | 670.5342688 | 19 | 0 | 4.5 | 93 | 7.6
115-18-4 | 2-Methyl-3-buten-2-ol | C5H10O | 86130 | 129.9 | 22 | 106.6 | 0 | 528.9678393 | 42 | 0 | 3.2 | 106.6 | 3.2
78-83-1 | 2-methylpropan-1-ol | C4H10O | 74120 | 107.89 | 32 | 105 | 15 | 685.3750675 | 39 | 0 | 1.8 | 90 | 9.7
534-22-5 | 2-methylfuran | C5H6O | 82100 | 65 | 37 | 103 | 16.9 | 392.2046285 | 26 | 0 | 1.4 | 86.1 | 0.2
625-86-5 | 2,5-Dimethylfuran | C6H8O | 96130 | 93.5 | 19 | 101.3 | 13.2 | 330.8020389 | 28 | 0 | 1.6 | 88.1 | 12.7
100-66-3 | Methoxybenzene | C7H8O | 108140 | 155.5 | 24 | 103.3 | 11.3 | 428.1486961 | 32 | 0 | 2.1 | 92 | 9.6
79-20-9 | Acetic acid, methyl ester | C3H6O2 | 74080 | 56.8 | 26 | 120.3 | 0 | 438.7149028 | 31 | 0 | 1.9 | 120.3 | 18
141-78-6 | Acetic acid ethyl ester | C4H8O2 | 88110 | 77 | 28.5 | 118 | -2.3 | 399.5006242 | 37 | 0 | 3.4 | 120.3 | 13.2
123-86-4 | Butyl acetate | C6H12O2 | 116160 | 126.1 | 46 | 100.8 | 0.6 | 369.3181818 | 35 | 0 | 6.8 | 100.2 | 12.9
107-87-9 | 2-pentanone | C5H10O | 86130 | 101.7 | 41.2 | 105.7 | 2.3 | 445.8376872 | 18 | 0 | 15.4 | 103.4 | 4.2
67-64-1 | 2-Propanone | C3H6O | 58080 | 56 | 30.2 | 108 | 6 | 538.9118457 | 41 | 0 | 12.4 | 102 | 3.8
464-06-2 | 2, 2, 3- Trimethyl-butane | C7H16 | 100200 | 80.8 | 19.8 | 112 | 11 | 288.4231537 | 42 | 0 | 11.8 | 101 | 67.2
3387-41-5 | 4-methylene-1-(1-methylethyl)bicyclo[3.1.0]hexane | C10H16 | 136230 | 164 | 30 | 106.5 | 0 | 281.8762387 | 26 | 0 | 5.6 | 106.5 | 9.1
108-67-8 | 1,3,5-Trimethylbenzene | C9H12 | 120190 | 164.7 | 31 | 120 | 0 | 395.207588 | 52 | 0 | 2.3 | 120 | 1.2

## Slide 12: Miles Merit Function #1 (K=0.5)
This is fiction: the ONLY purposes are to have some way to test the optimizer and
to see what type of data we could get out of it once the properties are available

## Slide 13: Miles Merit Function #2 (K=20)
This is fiction: the ONLY purposes are to have some way to test the optimizer and
to see what type of data we could get out of it once the properties are available

## Slide 14: Cost vs merit
This is fiction: the ONLY purposes are to have some way to test the optimizer and
to see what type of data we could get out of it once the properties are available
K=0.5
K=20

## Slide 15: Next steps for co-optimizer
Non-linear blending functions
Determine appropriate input list
  20, 40, all….?
  Blends with constrained ratios of pure components and costs)
Real property data
Integer constraints and objectives
Uncertainty of inputs (stochastic optimization)
  Properties, blending model, coefficients in merit function
Blending model
  Surrogate for non-linear model, or evaluate in situ
Coefficients in merit function
Alternative frameworks
  Julia / JuMP
  Explore GA + barrier method as alternative to IPOPT (robustness vs cost)
Multi-objective optimization
  Need additional engine merit functions
Develop and coordinate task schedule
  NREL, ANL, LBNL all participating in task

## Slide 16: Timeline and linkages
Fuel property database: 12/1
Blend stock composition: 12/1
ASSERT continuous costs: 1/9
Preliminary integer metrics 1/17
ASSERT integer metrics: 2/1
MT integer metrics 2/21
Strategy for protecting inputs 2/1-2/28
Initial release 12/23
Most promising components based on linear blending and MMF 2/14
Cost-MMF-ASSERT-MT trade space analysis 3/10
Report/toolset for 18mo decision point available 3/23

## Slide 17: Task risks
Aggressive schedule sensitive to staffing availability, technical setbacks
Currently no plan to deal with missing data
Linear blending model may restrict applicability
Work front-loaded in FY17; issues under CR (ok at NREL)
Usage model evolving as toolsets developed, may need to rework

## Slide 18
Task G.4: Develop optimizer inputs ($750K $400K)
Objectives: Convert data for engine performance (‘cloud of points’ in property space) into smooth function(s) for optimizer Bounded performance estimate for given properties Identify new test matrix to most reduce uncertainty Approach: Determine best interpolative / extrapolation function from candidates including ‘Miles’ merit function, machine learning algorithms, etc. Bayesian parameter estimation to find coefficients Hierarchical construction so new data points can be added and candidate points evaluated for impact
Team: Simulation Toolkit Development Task Summary New Continuing from FY16 Proposed FY17 Funding: BETO _____ VTO_____ Lead PI (lab): Grout (NREL; $250K $175K) Participating Labs: LBNL(250K $175K), SNL(100K), ANL(100K), LLNL (50K) Thrust I Thrust II Relevant to Both Priority: Base Margin Over Target
Milestones and Outcomes: FY17/Q1 Function ingesting key Co-Optima experimental/simulation performance data FY17/Q2 Set of key new test points Outcomes at Base Funding: Improved Merit function based on key engine data Recommended new test points on basis of optimizer results with uncertainty Margin: Solid mathematical framework to refine engine experiment and simulation test matrix for greatest impact on uncertainty reduction Add additional data (sim and exp.) to merit function Coupling to 0D kinetics solve to use non-linear blending models based on surrogate fuels
Budget:
Project | FY16 | FY17 | FY18 | FY19
VTO | - | B: $325K M: $750K | TBD | TBD
Project Type | Directed |  | Project Status | Continuing
Key link to FY17 Research Thrusts Closely linked to thrusts #1 (development of Thrust 1 merit function), #3 (critical input for co-optimizer), #6 (unifying framework to coordinate engine experimental and simulation data, develop optimal test points to develop understanding and reduce uncertainty). Key links to other teams AED and TD (data inputs, new test points output ) and FP/LGGF (identification of optimal fuel structures)
Notes: This is the part that rigorously ingests the engine and simulation datasets and puts error bounds on the resulting merit function evaluation for an arbitrary property combination necessary as an input to make this optimizer valuable – especially for choosing new test points that focus research where it most effectively builds confidence in the estimate to distinguish between the multiple possible optima.
Base breakdown: NREL $175k; LBNL $150k;
Margin increments: NREL $75k; LBNL; $100k; SNL$100k; ANL $100K; LLNL $50K. Note that the margin funding requested under G.4 represents several different approaches to develop or improve the inputs needed by the Scenario Optimizer. If the margin funding were to be available, it is recommended that the proposed research is prioritized at that time to increase the impact of the additional funds, which may require concentrating the effort at fewer labs.

## Slide 19: Developing an engine merit function
Need to collect engine test data that probes relationship between properties and performance
Sweep out surface of maximum engine efficiency obtainable for a given property set
Embedded optimization problem where engine operating parameters (spark timing, boost, CR, etc) are tuned for best performance
Part load points also important to get drive cycle efficiency merit

## Slide 20: Developing an engine merit function
Need to identify what the function engine/simulations observe is and how it maps to merit function
Engine experiments – cloud of points in property space for various engines and operating conditions
Simulation experiments – sensitivities at same (?) conditions
Varying fidelity of things we could
Curve fit / regression for functional form
Bayesian UQ/UP
Feed into stochastic optimization
Identify test points that would constrain optimization (possibly not relevant for general engine development)

## Slide 21: Developing an engine merit function
Bayesian UQ can map out distribution of parameters consistent with data
Sampling procedure (MCMC, particle filter, etc…):
Choose a sample point (paramter value)
Evaluate function
Compute liklihood from experiment(s)
  Need experiments corresponding to “merit” with uncertainties
Example from H2-air kinetics, 4 parameters

## Slide 22: Timeline
Q1FY17: Function ingesting key Co-optima experimental/simulation performance data
Q2FY17: Set of key new test points
Agree (or not) if mapping out merit function is priority
Functional form of merit function (now... done?)
Need to catalog existing engine data that measures merit (early Q1)
Identify engines (done) and conditions for sensitivity calculation (early Q2) and coordinate with engine test plans
Strategy for how to account for different engine designs